## Slide 1: Automation Operation Concept For Next CNES Missions

## Slide 2
History of ISIS
ISIS Product Line
  Architecture
  Subsystems
  Main drivers
ISIS Operational Concept
  From Assembly to Deployment
  During operational phase
Conclusion : First feedback
Automation Operation Concept For Next CNES Missions

## Slide 3: 3 partners : Thales Alénia Space, Airbus Defense and Space, and CNES
ISIS : Initiative for Space Innovative Standard

## Slide 4: ISIS Standard
Automation Operation Concept For Next CNES Missions
ISIS Standard includes :
Standard documentation
Typical mission documents to be tailored
Covering :
  All aspects of the platform and command control ground segment
  The interfaces within ISIS components and with external entities
ISIS Product Line

## Slide 5: ISIS Product Line : software architecture
Daemons
C++ / Python
LibCom
including Directory Service
ZeroMQ
Redis
GUIs
C++ / Python + Qt/JavaScript
Scripts
Python
CONFIG
Processings
C++ / Python
Automation Operation Concept For Next CNES Missions
SOA architecture with components
Standards based design
Follows CCSDS MO (SM&C) standard
  Service Oriented components
  Talking on a Message Abstraction Layer
  Modular approach
  Simple function addition/removal (tailoring of the CCC)
ISIS Standard implementation:
  XTCE, SLE, CCSDS TM/TC, PUS (subset), COP1
  Other specific ISIS interfaces
ISIS Product Line
~ 100 components

## Slide 6: ISIS Product Line : subsystems
ISIS Product Line
Automation Operation Concept For Next CNES Missions
6
Automation : operations scheduling by rules or on the fly, full control centre automation
Monitoring & control
TM acquisition and processing
TC sending
PUS services
Visualisation
Data real time and offline visualisation (TM, mimics)
Flight Dynamics
Orbit, attitude, Events prediction
Operations support
Event management
Memory image management
Reports
DataStore
Data archiving, management, consultation
Trend analysis
Infrastructure
GUIs, users authentication, global system monitoring, external exchanges, time management, printing …

## Slide 7: From Assembly to Deployment
ISIS Operational Concept

## Slide 8
Automation Operation Concept For Next CNES Missions
Multi Targets
Control Command Center
Main Control Room
Fly Dynamics Standalone
Expert Computer
On Call Computer
Assembly, Integration, and Test
DMZ
ISIS Product Line is designed to cover :

## Slide 9
Automation Operation Concept For Next CNES Missions
ISIS Product Line is designed to cover :
Multi Missions
SWOT
MERLIN
CERES
Argos 4 NG
SVOM
NeSS
…
One mission target is a product line implementation built on :
  A selection of common and mission specific components delivered by the IT company or CNES teams
  And a deployment of these components on a set of Virtual Machines
A topology

## Slide 10: Example of the SWOT CCC target implementation cycle of life
10
SWOT assembly
SWOT
Spectre
Dépendencies
SWOT + Spectre
CNES Generic Missions (AIT, Scientific, Military,…)
ISIS Product Line = RPMs, scripts, configurations
SWOT
Merlin
SWOT + Merlin
CERES
SVOM
Automation Operation Concept For Next CNES Missions
CERES
CERES
SWOT CCC target

## Slide 11: Management of this multi-mission/target process
Automation Operation Concept For Next CNES Missions
version_configuration:
operational:
mission_system_version: "1.0"
fds_system_version: "3.1.6"
ccc_system_version: "8.14.2b"
....
validation01:
mission_system_version: "2.0"
fds_system_version: "3.1.7"
ccc_system_version: "8.15"
- hosts : WebServer
tasks:
- name : Start HTTP server
service:
name: "{{ httpd_service_name }}"
state: started
- hosts : Database
roles:
- role: InstallMariaDB
To manage all the piece of software, scripts, configuration files …
To manage the configuration and to deploy automatically a mission target

## Slide 12: During operationnal phase
ISIS Operational Concept

## Slide 13: Operationnal concept driver before software development
  Automated but :
Check of the right behavior
Sequence of operations to perform
Supervision of on-going operations
Switch to manual by the operators
Automation Operation Concept For Next CNES Missions
Plan the itinerary
And possible manual interruption
Automation : operations scheduling by rules or on the fly, full control centre automation

## Slide 14
All operations (complex or simple) can be automated
BUS
Connection
DataStore
Acquisition
Decom’
Packets
Frames
Decommuted parameters
Automation Operation Concept For Next CNES Missions
  Either ground/board or ground operation
  From high level function (eg. connect TM flow procedure) to low level operation using all the API exposed by all the components (eg. getParameterValue(CPU_load) )
  Example:

## Slide 15: Rule based scheduling
Automation Operation Concept For Next CNES Missions
  Real time reaction to events based on reflexes rules (onboard alarm, safe-mode, critical failure,…)
  Offline schedule based on expected events (eclipse, station change, maintenance) , dates, internal variables …
  Real time conditional execution (based on CCC or satellite parameters)

## Slide 16: Operations orchestration and supervision : level 1
Automation Operation Concept For Next CNES Missions
System view of the operations
with high level control if needed

## Slide 17
Automation Operation Concept For Next CNES Missions
Operations orchestration and supervision : level 2
Group of operations zoom view

## Slide 18
Automation Operation Concept For Next CNES Missions
Operations orchestration and supervision : level 3
Detail view of an operation
with step by step control if needed

## Slide 19: Operations orchestration and supervision : scalability
Fully configurable
  Within the 3 levels : system, group of operations and operations
  Able to cope with any mission choices
Very simple to add new operations
  Mostly written in Python,
  Can be any executable
Possibility to schedule a new operation at any time
  Depending on pattern matching on logbook events
  Logbook events sent by any component of the product line
Automation Operation Concept For Next CNES Missions

## Slide 20: Conclusion
ISIS Operational Concept

## Slide 21: ISIS Product Line : first feedback
Automation Operation Concept For Next CNES Missions
A real upgradeable and scalable micro architecture
  Easy to add new functionality (e.g. 4 and 5 specific components added for the first missions, to compare to ~100 common components)
  Choose the distribution of the components depending on the deployment and hardware characteristic (Control Command Center, Main Control Room, AIT Testbed ..)
  Possibility to adapt hardware to specific target performances
Improvement of the automation subsystem, scalable within the 3 levels and able to react in real time
Ready for various multi missions : typical ones (1 and 3 satellites), constellation, AIT …
But new operational way of thinking to compare to “old CCC” : from MMI control to deamon execution with MMI for supervision