## Slide 1: Building a Science-Driven Mission Planning Tool with OSS JMARS
ISOW 2019 • May 3-4, 2019
Christian Schaller • schaller@lpl.arizona.edu
Lead Software Developer, Planetary Image Research Lab
Lunar and Planetary Lab
The University of Arizona
Tucson, Arizona, USA

## Slide 2: Roadmap
Science-driven mission planning
JMARS
OSS JMARS
Example: Data supplier for existing shape layer
Example: Customized shape layer
Example: Mission planning layer
Java SPICE
Summary

## Slide 3: Science-driven mission planning

## Slide 4
Mars Reconnaissance Orbiter & HiRISE (NASA)
Trace Gas Orbiter & CaSSIS (ESA, Roscosmos)
Scan | Push-broom
Detector | 14 CCDs (2, 10, 2 config)
Detector Size | 2048 x 128, 14 bit/px
Ground Scale | 30 cm/px
Swath Width | 6 km
Colors | 3 (red, blue-green, nir)
Scan | Push-frame
Detector | 1 CMOS
Detector Size | 2048 x 256 strips, 14 bit/px
Ground Scale | 4.6 m/px
Swath Width | 9.4 km
Colors | 4 (pan, red, blue-green, nir)
HiRISE
CaSSIS
Uni. Bern
ESA/ATG medialab
NASA
NASA/JPL/Ball Aerospace

## Slide 5
Is it safe to land here?
PSP_007448_2475 • NASA/JPL/University of Arizona
What’s going on here?!?
ESP_013049_0950 • NASA/JPL/University of Arizona
How did these streaks form?
ESP_058514_2140 • NASA/JPL/University of Arizona
What’s the best route for this rover?
MER-A “Spirit”
ESP_021925_1650 • NASA/JPL/University of Arizona

## Slide 6
To answer questions like these, you might need…
  Elevation/topography data (e.g., MOLA)
  Albedo data (TES)
  Thermal data (THEMIS)
  Minerology maps (TES again)
  Orbit tracks
  Previously acquired images
  Region-of-interest outlines
  Location of existing hardware
  Planned traverse paths
…all displayed in one view
…a geographic information system (GIS) application

## Slide 7: JMARS

## Slide 8: JMARS: A Java-based multi-body GIS app
Developed at ASU (in Phoenix, AZ – definitely not to be confused with UA in Tucson, AZ)
Originally for Mars, but now supports most large, rocky bodies in the Solar System plus a few asteroids
Data layers
  Dozens of global base maps from various instruments
  Image stamp layers
  Ground track layers
  Nomenclature
  General shape layer
  Crater counting layer
  …each with customizable layer transparency
Used by MRO, OSIRIS-REx, TGO/CaSSIS…
https://jmars.asu.edu

## Slide 9
The public version of JMARS

## Slide 10
JMARS for MRO (Mars Target Tool, MTT) – HiPlan for HiRISE – Commissioned

## Slide 11
OSS JMARS for CaSSIS: PLAN-C

## Slide 12: OSS JMARS

## Slide 13: Open-source (OSS) JMARS
ASU has an open-source version of JMARS
  https://jmars.mars.asu.edu/open_source
  Subversion repo: http://oss.mars.asu.edu/svn/jmars/
Includes all the core capability of the public JMARS
Robust set of APIs
  API documentation a little sparse
Underlying layer base classes feature
  Multiple off-screen graphics buffers
  MVC model
  Threaded execution
Several example layers for use as starting points
Current version (r31) similar to current public version
  PLAN-C actually built on r3, which looks more like MTT/HiPlan
  Will transition PLAN-C to current OSS JMARS “one of these days”

## Slide 14: Example: Data supplier for existing shape layer
Easy!

## Slide 15
The shape layer’s primary data sources are defined by a very simple API
TRUE
FALSE

## Slide 16
TRUE
Spacecraft event points file source
#Event,Time
MSL Entry,2012-219T05:10:46.000
HiRISE CPMM power,2012-219T05:11:10.480
MSL guidance start,2012-219T05:11:31.900
MSL parachute deployment,2012-219T05:15:05.100
HiRISE image start,2012-219T05:16:19.482
HiRISE MSL heat shield,2012-219T05:16:39.353
HiRISE MSL lander,2012-219T05:16:42.178
HiRISE image end,2012-219T05:17:02.162
HiRISE readout start,2012-219T05:17:35.617
MSL TD,2012-219T05:17:56.900
HiRISE readout end,2012-219T05:30:35.817
Caveat: SPICE required to turn times into coordinates!

## Slide 17
FALSE
HiRISE target database non-file source

## Slide 18: Example: Customized shape layer
A Little Trickier!
(This layer is the work of Guy McArthur, Data Applications Developer, PIRL/LPL/UA!)

## Slide 19
CaST web app: CaSSIS Suggested Targets

## Slide 20
Customizing the shape layer requires a bit more work…
Four base classes to extend
  …plus your own data classes
Some functionality not directly available
  Needed to use Java reflection to get to some functions
  Always a little risky
You DO get the nice MVC and thread management of the JMARS layer model, though!

## Slide 21: Why not use a custom data source?
We needed much more control over this layer
Cannot be editable
  CaST web app is the one and only source of targets
  Can’t give PLAN-C user the impression they can edit in PLAN-C!
Need a combination of file and database sources
  Drag-and-drop or copy/paste a list of targets
  Directly search the target database
Need to display a more complex table
  Target database includes sites plus series variants!
  E.g., a target for stereo has two variants, forward and reverse look
  A seasonal target may have 2, 3, 4, 10, 20 or more variants

## Slide 22
We gained a lot from the base class, but could customize it to our needs…relatively easily!

## Slide 23: Example: Mission planning layer
Quite
Complicated!

## Slide 24: Mission planning layer: complex, complicated
The mission planning layer will likely be the most complex and challenging part of this process
Requirements
  Display orbit tracks, including off-nadir extent
  Display planned observations’ footprints
  Display exclusion zones
  Import from file or database
  Store plan in database, export to file for third-party use
  Add/remove observations from the plan
  Control camera settings
  Model data volume use and data transfer rates
  Check for flight/ops rule violations
  Present timeline view of plan
No existing API for most of this!
  Can use the built-in ground track layer as a starting point, though
No existing SPICE solution!

## Slide 25
CaSSIS planning layer map features
Solid yellow line: day, no exclusions
Blue box: CaSSIS image footprint
Tiny magenta box: TGO at image center
Pink box: CaST layer beneath
Green box: off-nadir extent of selected orbit
Orange highlight: no targeted, nadir warning
Red highlight: no imaging allowed
Dashed line: night
Panner view (JMARS core)
Main view (JMARS core)

## Slide 26
Adding an image to the plan
Adding here, inside outline of target 600, on a night segment inside an ”observation wheel off-load” zone
Coordinates
Time, lighting
Exclusion warning for nadir, violation for targeted
If parenting to target 600…
If not parenting to a target

## Slide 28
COGG: CaSSIS Observation Generation GUI (after HOGG: HiRISE…)

## Slide 29: Java SPICE

## Slide 30: SPICE in Java
NAIF SPICE toolkit used for spacecraft/body position, velocity, pointing, timing
  https://naif.jpl.nasa.gov
Fortran, C, IDL, Matlab officially supported
When we started, there was no widely available Java toolkit
  NAIF: JNISPICE, flagged as an “alpha-test”
  ASU: JSPICE (used in MRO tools MTT, HiPlan), not released
    Destined for public release, I believe
Obviously we rolled our own: UA-SPICE
  Large effort, diverted some resources from PLAN-C proper
  Useful in other contexts, useful learning experience
  Likely open-source it
NAIF’s JNISPICE is now “considered of sufficient quality to be released to interested persons”
Strongly recommend pursuing NAIF’s solution
  I’ll likely replace UA-SPICE in PLAN-C with JNISPICE in the future

## Slide 31: Summary

## Slide 32: Summary
JMARS is a capable, Java-based GIS application suitable for science-driven spacecraft mission operations
The open-source version (OSS) can be extended to your particular needs with varying degrees of effort
  Custom data sources for the shape layer require the least effort
  Customizing an existing layer requires more effort but is a viable solution in some cases
  A fully functional mission planning layer with resource modeling, flight rules, etc., can tap into everything provided by the JMARS core, but may require considerable effort
Probably best to use NAIF’s own JNISPCE as a SPICE solution
HiRISE: https://hirise.lpl.arizona.edu | CaSSIS: http://cassis.unibe.ch
JMARS: https://jmars.asu.edu | NAIF/SPICE: https://naif.jpl.nasa.gov

## Slide 33
HIGH RESOLUTION IMAGING SCIENCE EXPERIMENT
uahirise.org